ILYUSHIN IL-2/IL-2M

# STORMOVIK

A heavily armored ground-attack monoplane, the backbone of the Soviet ground-attack units in WWII.  It's deadly efficiency originated not only from it’s powerful weapons, but also from the unprecedented armoring of all vital elements: pilot cockpit, engine, cooling system, internal bomb bays.  Other earlier contemporary aircraft (with few exceptions) had armor as a addition to the airframe, and suffered from its passive weight.  In the case of the Il-2, armor became a part of aircraft’s structure, performing a substantial part of structural functions.  This resulted in great weight savings.  Plus, the armor itself was specially designed to withstand small shells, bullets and shrapnel.  This protection allowed pilots to perform multiple bomb/strife runs over a target area, allowing them to spend more time aiming...

General layout of the Il-2 made it maneuverable enough to allow skilled pilots to perform active air-to-air combat against fighters... Unfortunately there was not enough time for pilots to get enough training, and they had to learn it in real combat, paying a heavy toll in lives.

The first production modification of Il-2 had no rear gunner position.  This was just ordered by Kliment E. Voroshilov (then Commissar and Chairman of the Red Air Force), who felt that the rear gunner position is not necessary.

There came heavy losses from fighters in the first months of the Great Patriotic War, when Il-2's were forced to operate without both escort and rear defense.  Despite the excellent armor and firepower of the Stormovik, German fighters had enough time for multiple attacks, especially when Stormoviks were on target.

| MANUFACTURER | Ilyushin |  | SPECIFICATIONS | metric | english |
| --- | --- | --- | --- | --- | --- |
| TYPE | IL-2 / IL-2M |  | WEIGHT | 4200kg | 9240 lb |
| FUNCTION | Attack |  | WING SPAN | 14.6 meters | 47.90 ft |
| YEAR | March, 1941 |  | LENGTH | 11.6 meters | 38.06 ft |
| CREW | 1 (IL-2) 2 (IL-2M) |  | HEIGHT | 4.11 meters | 13.48 ft |
| ENGINE | 1600hp Mikulin |  | WING AREA | 83.5 sq meters | 898 sq ft |
|  |  |  | SPEED | 433 km/h | 264 mph |
|  |  |  | RANGE | 740 km | 451 miles |
|  |  |  | CEILING | service 4000m | 13,100 ft. |

## IL-2

### IL-2M

Fuselage:

- 3/16" ply firewall (F2)

- 1/8” Lite-Ply or thin ply Formers, F-3 thru F-8

- 1/8”x1/4 stringers

- ½” Balsa “chin” block, F-2 to F-3

- 3/32" fuse sheeting

- Stab Base made from 1/8” Lite-Ply.

- Canopy can be built-up from 1/16” Balsa or formed plastic

Tail Feathers:

- The tail is set for stick building to lower weight.

- Construct with ¼” x ½” Balsa, reinforced with 1/8” x ¼” Balsa Sticks.

Wing:

- 3/32" ribs and W-3 Gussets,

- 1/8”x1/4” spars,

- 3/16” TE doubler,

- 5/16” x 1.25” TE ,

- ¼” x 1/2” LE.

- 1/16” x 3/16” Cap Strips, W4 to W7,

- Build in about 3/8” washout from W3 to W7.

- Wing sheeting should be 1/16”:

- LE to spars,

- 1" wide TE

- Full sheeting from middle of W3/4 to W3/4.  Note, if the upper sheeting is continuous and the lower wing chine is made from a Balsa block, the wing should be strong enough to eliminate taping the center seam.

Materials:

|  |  | # needed | # needed | Balsa USA | Balsa USA | Price @ | Price for |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Size | Material | for 1 plane | for 3 P40s | P/N | Price @ | Plane | 3 Planes |
| 1/8x1/4x48 | Bass/Spruce | 2 | 6 | 300 | 0.38 | 0.76 | 2.28 |
| 1/8x1/4x48 | Balsa | 3 | 9 | 160 | 0.22 | 0.66 | 1.98 |
| 1/4x1/2x48 | Balsa | 2 | 6 | 168 | 0.42 | 0.84 | 2.52 |
| 1/8x3x30 | Balsa | 1 | 1 | 65 | 0.56 | 0.56 | 0.56 |
| 1/16x4/48 | Balsa | 3 | 9 | 51 | 0.97 | 2.91 | 8.73 |
| 5/16x1.25x36 | Balsa | 2 | 6 | 119 | 0.49 | 0.98 | 2.94 |
| 3/16x3/16x48 | Balsa | 1 | 3 | 163 | 0.24 | 0.24 | 0.72 |
| 1/2x4x36 | Balsa | 1 | 1 | 33 | 3.00 | 3.00 | 3.00 |
| 3/32x4x48 | Balsa | 5 | 15 | 52 | 1.21 | 6.05 | 18.15 |
| 3/32 6x12 | 5 ply Birch | 1 | 3 | B347 | 2.76 | 2.76 | 8.28 |
| 3/16 6x12 | 4 ply Birch | 1 | 1 | B349 | 1.85 | 1.85 | 1.85 |
|  |  | Balsa USA | P.O. Box 164 |  | Sub-Total | 20.61 | 51.01 |
|  |  |  | Marinette, WI 54143 |  | S&H | 6.49 | 6.49 |
|  |  |  | 1-800-225-7287 |  | Total | 27.10 | 57.50 |

----------------